## Slide 1
OPENSTRANDSTUDIO · LAYER PANEL
Hiding the group panel
Option B in three flavors: the control lives on the group column itself.
Chapter 1 B1 hover pin with peek · Chapter 2 B2 divider tab · Chapter 3 B3 icon rail
Create
Group 1
1_1
1_2
Group 2
Notes: Title slide. Three UX designs for the same job: get the 140 px group column out of the way so the canvas gets the room, with the control located on the column itself.

## Slide 2
Group panel · option B
2
WHERE WE START
The group column is 140 px that never moves
Create Group
Group 1
1_1
1_2
Group 2
canvas 750 px · layer panel 350 px · group column 140 px (window 1100 px)
1
2
3
140 px
group column, fixed width
350 px
layer panel minimum
0
ways to hide it today
1 Group column: the Create Group button and the group tree, a fixed 140 px inside the layer panel.
2 The inner splitter between the layer list and the group column is locked: no collapse, no drag.
3 The outer splitter can move, but the panel cannot go below 350 px, so the canvas never gets the room back.
Notes: Today the layer panel is two columns: the layer list and the group column. The group column is exactly 140 px and the splitter between them is disabled in code. Users who rarely use groups lose that width permanently.

## Slide 3
Group panel · option B
3
SHARED BY ALL THREE
Ground rules every variant follows
1
Canvas gains the room
When groups are hidden, the layer panel minimum drops from 350 px toward 210 px and the canvas grows. The outer splitter still lets you drag the layer list wider.
2
Remembered between sessions
One line in the settings file, written with the same read-modify-write the Tabs edge position uses, so the settings dialog keeps its own lines.
3
One shortcut, everywhere
Ctrl+G (Cmd+G on macOS) toggles the same state as the on-screen control. The app has no shortcuts yet, so this is the first.
4
Hebrew mirrors
In Hebrew the whole window flips: the layer panel is on the left, the group column at the far left. Every control mirrors with it.
5
Compact screens keep working
The narrow-window path that slims the panel treats a hidden group column as zero width instead of 140.
6
Same look in every theme
Controls take their colors from the group panel theme table so default, light and dark all read the same.
Notes: These six rules are identical across B1, B2 and B3, so the chapters only cover what differs: the control, the states, and the interaction steps.

## Slide 4
CHAPTER 1
B1 · Hover pin with peek
A faint pin in the far corner of the group column. Press it and the column gets out of the way; hover the edge to peek it back; press again to stick.

## Slide 5
Chapter 1 · B1 hover pin with peek
5
B1 · AT A GLANCE
The control: a pin that lives in the corner
Create Group
Group 1
1_1
1_2
Group 2
pinned · canvas 750 px · layer panel 350 px
1
Where
Bottom far corner of the group column: the outer window edge, below the tree, out of the way of the layer buttons.
At rest
Faint, about a third opacity. It brightens to full when the mouse is over the group column, so it never competes with the tree.
What it means
Upright pin = pinned in place (today's layout). Tilted pin = auto-hide. One glyph tells you which mode you are in.
What it does
Toggles between pinned and auto-hide. In auto-hide the column lives off-screen and can be peeked by hovering the edge.
Notes: The pin is the only new visible element and it is deliberately quiet. Corner placement follows Visual Studio and JetBrains tool windows, where the pin sits in the panel header; here it sits at the bottom because the top of the column is the Create Group button.

## Slide 6
Chapter 1 · B1 hover pin with peek
6
B1 · STATES
Three states, one pin
Pinned
Create
Group 1
1_1
1_2
Group 2
canvas 750 · panel 350
Default. Layout as today. Pin faint, upright.
Auto-hide
canvas 890 (+140) · panel 210
Column off-screen. A 10 px edge strip with a label and a group-count badge marks it.
Peek
Create
Group 1
1_1
1_2
Group 2
canvas 890 · overlay 140
Hovering the strip slides the column over the canvas. Nothing else moves. Pin shows tilted.
Transitions Pinned → Auto-hide: click the pin. Auto-hide → Peek: hover the edge strip for 200 ms, or click it. Peek → Auto-hide: move the mouse off the panel. Peek → Pinned: click the pin while peeked. Anywhere: Ctrl+G toggles pinned and auto-hide.
Notes: Auto-hide and peek are the same stored state; peek is a transient overlay. Only pinned vs auto-hide is persisted.

## Slide 7
Chapter 1 · B1 hover pin with peek
7
B1 · STEP BY STEP
Hide, peek, and pin it back
1
Hover the group column
The pin brightens from faint to full in the bottom far corner. Tooltip: "Auto-hide groups".
2
Click the pin
The column slides out toward the window edge (250 ms). The layer panel narrows to 210 px and the canvas widens by 140 px. A 10 px edge strip remains, reading GROUPS with a badge showing the group count.
3
Hover the edge strip
After a 200 ms hover delay the column slides in over the canvas as an overlay with a soft shadow. The layer list and canvas do not move. A click on the strip does the same without waiting, for trackpads and touch.
4
Work in the peeked panel
Create Group, expand and select groups, drag layers in. The overlay stays open while the mouse is inside it or a menu from it is open.
5
Move away
Leaving the overlay for 220 ms slides it back out. No click needed.
6
Click the pin while peeked
The pin is tilted here. Clicking it pins the column back into the layout: panel 350 px again, canvas gives the 140 px back.
Notes: Six steps cover the whole loop. The hover delay in step 3 is the important number: without it, a mouse travelling to the vertical scrollbar of the layer list would flash the panel.

## Slide 8
Chapter 1 · B1 hover pin with peek
8
B1 · INTERACTION DETAILS
The small rules that make auto-hide feel right
Create Group
Group 1
1_1
1_2
Group 2
peek overlay: 140 px over the canvas, shadow on the inner edge
1
2
3
1
Edge strip
Full height, 10 px, divider gray. Rotated GROUPS label and a magenta count badge keep the hidden feature visible. Hover 200 ms or click to peek.
2
Peek overlay
Drawn above the canvas, anchored to the outer edge. Never resizes the canvas, so drawing is not interrupted. Closes 220 ms after the mouse leaves, or on Escape.
3
Pin
Faint at rest, full on hover, tilted 45° in auto-hide. Tooltip flips between "Auto-hide groups" and "Pin groups". Reachable with Tab and Space.
Touch and keyboard
Tap on the strip peeks; tap outside closes. Ctrl+G toggles pinned and auto-hide. No hover anywhere in the keyboard path.
Hebrew
Strip, pin corner and slide direction mirror to the left edge, same as the layer panel already does.
Persistence
GroupPanelMode: pinned | auto in the settings file. Peek is never saved.
Notes: The overlay is the piece that needs the most care in Qt: it is a top-level child widget of the main window positioned over the canvas, shown and hidden with a QPropertyAnimation on its x position and two QTimers for the hover delays.

## Slide 9
Chapter 1 · B1 hover pin with peek
9
B1 · ASSESSMENT
B1: elegant once learned, hover-dependent
For
Nothing added to the layout at rest; the pin is quiet until needed
Groups stay one hover away, so hiding them costs almost nothing
Full 140 px back to the canvas
Pattern known from Visual Studio, JetBrains, Windows taskbar
Against
A control that hides itself is hardest to find the first time
Peek needs a hover delay and a click fallback or it flashes
Three states; the tilted pin is the only visible clue
Overlay does not exist on touch without the click fallback
What it takes to build
Pin button as a child of the group column, opacity driven by enter/leave events
Reparent the group column into an overlay widget above the canvas in auto-hide; back into the inner splitter when pinned
Edge strip widget with label and badge
Two QTimers (200 ms open, 220 ms close) and one x-position animation
Three-value setting, Ctrl+G, translations, RTL
Effort: medium · Risk: medium
Canvas +140 px
Hover dependent
Effort medium

## Slide 10
CHAPTER 2
B2 · Tab on the divider
The divider between the layer list and the group column becomes a real splitter handle with a chevron tab. Click to collapse, drag to resize, double-click to toggle.

## Slide 11
Chapter 2 · B2 divider tab
11
B2 · AT A GLANCE
The control: a tab on a divider you can drag
Create Group
Group 1
1_1
1_2
Group 2
›
shown · canvas 750 px · layer panel 350 px · divider 6 px
1
2
Where
On the 6 px divider between the layer list and the group column, at mid-height. Always visible.
Tab
16 × 48 px, gray at rest, magenta on hover. The chevron always points the way the column will move: › to hide, ‹ to show.
Divider
Becomes a live splitter handle: drag it to give the group tree more room for long names, or less. Double-click toggles collapse.
Hidden state
Column width 0. The divider and tab stay at the window edge as the way back, so the canvas gains 134 px.
Notes: This is the Finder / Explorer / IDE sidebar pattern. The code already has a QSplitter here; it is just disabled. B2 turns it on and puts a tab on its handle.

## Slide 12
Chapter 2 · B2 divider tab
12
B2 · STATES
Two states, plus any width in between
Shown
Create
Group 1
1_1
1_2
Group 2
›
canvas 750 · panel 350
Default. Chevron points at the column: ›
Hidden
‹
canvas 884 (+134) · panel 216
Column collapsed to 0. Divider and tab sit at the window edge. Chevron flips: ‹
Dragged wider
Create Group
Group 1
1_1
1_2
Group 2
›
canvas 680 · panel 420 · groups 210
Any width between 100 and 260 px. Long group names stop being clipped. Width is remembered.
Transitions Shown ↔ Hidden: click the tab, double-click the divider, or Ctrl+G. Shown → Dragged: drag the divider; below 100 px it snaps to Hidden. Hidden → Shown: click the tab; the column returns at its last width.
Notes: Dragging is the bonus B2 gives for free: the app has never let anyone widen the group tree.

## Slide 13
Chapter 2 · B2 divider tab
13
B2 · STEP BY STEP
Click, drag, double-click
1
Find the tab
Mid-height on the divider, always visible. Hovering turns it magenta and the cursor becomes a pointer. Tooltip: "Hide groups".
2
Click the tab
The column collapses toward the window edge (250 ms). The divider and tab move with it and stop at the edge. Layer panel 216 px, canvas +134 px. Chevron flips to ‹, tooltip "Show groups".
3
Click again
The column comes back at the width it had before, not a default. Chevron flips to ›.
4
Drag the divider
The cursor changes to a resize cursor anywhere on the 6 px divider, not only on the tab. Drag left for a wider group tree (up to 260 px), right for narrower.
5
Drag past the snap point
Below 100 px the column snaps closed as if the tab had been clicked, and remembers the last width above the snap point.
6
Double-click the divider
Same as clicking the tab, for people who expect the Explorer behavior.

## Slide 14
Chapter 2 · B2 divider tab
14
B2 · INTERACTION DETAILS
Unlocking the splitter, keeping the layout
‹
hidden: divider + tab at the window edge, chevron flipped
1
2
1
The tab
A small QToolButton on the splitter handle, recentered on resize. Chevron flips with state; magenta hover uses the Tabs button colors.
2
The handle
Collapsible on the group side only; handle enabled; group width 100 to 260 px. Below the minimum on release it snaps to collapsed.
Widths that follow
Layer panel minimum = list minimum + 6 px divider + current group width. The compact-screen rule reads the live width, not the fixed 140.
Keyboard and touch
Tab is focusable; Space, Enter or Ctrl+G toggles. On touch the tab is the target; the 6 px divider is too thin for a finger, acceptable on desktop.
Hebrew
Divider sits on the left of the column; chevrons swap so they still point the way the column moves.
Persistence
GroupPanelVisible: true | false and GroupPanelWidth: 140 in the settings file.
Notes: The one risk in B2 is the compact-width arithmetic in the layer panel, which assumes the group column is exactly 140. Making it read the live width is a contained change.

## Slide 15
Chapter 2 · B2 divider tab
15
B2 · ASSESSMENT
B2: the conventional, always-visible choice
For
Always visible, always in the same place
Two states; the chevron says which way things move
Unlocks a wider group tree for long names, which nothing offers today
Finder, Explorer and IDE users already know it
Against
Keeps a 6 px divider: canvas gains 134 px, not 140
Compact-screen width rule must learn about a variable group width
Small target at mid-height, away from where the mouse usually is
Hidden means hidden: no peek without expanding
What it takes to build
Enable the existing inner QSplitter handle; allow collapse on the group side
Tab button parented to the handle, recentered on resize
Snap-to-collapse on release below 100 px
Compact-width rule reads the live group width
Two settings lines, Ctrl+G, translations, RTL
Effort: small · Risk: low
Canvas +134 px
No hover needed
Effort small

## Slide 16
CHAPTER 3
B3 · Collapse to an icon rail
A chevron at the bottom of the group column shrinks it to a 40 px rail: a + tile for Create Group and one tile per group. Groups stay one click away.

## Slide 17
Chapter 3 · B3 icon rail
17
B3 · AT A GLANCE
The control: a chevron that slims the column
Create Group
Group 1
1_1
1_2
Group 2
›
expanded · canvas 750 px · layer panel 350 px
1
Where
Bottom of the group column, centered, always visible. Same row as the layer panel's bottom buttons, where the mouse already goes.
What it does
Collapses the column to a 40 px rail instead of removing it. Chevron flips ‹ to expand.
The rail
Create Group becomes a 30 px + tile. Each group becomes a 30 × 24 tile with a short label (G1, G2...). The selected group's tile is highlighted.
Why
For people who use groups all day. The panel gets slim, but every group and the create action stay one click away.
Notes: B3 trades some canvas width for a collapsed state that is still useful. It is the browser-sidebar or Slack-workspace-rail pattern.

## Slide 18
Chapter 3 · B3 icon rail
18
B3 · STATES
Expanded, rail, and back with a selection
Expanded
Create
Group 1
1_1
1_2
Group 2
›
canvas 750 · panel 350
Default. Full tree and Create Group button. Chevron ›
Rail
+
G1
G2
‹
canvas 850 (+100) · panel 250 · rail 40
+ tile creates a group. G1, G2 tiles are the groups. Chevron ‹ expands.
Tile clicked
Create
Group 1
1_1
1_2
Group 2
›
canvas 750 · panel 350
Clicking G2 expands the column with Group 2 selected and scrolled into view.
Transitions Expanded → Rail: click the chevron or Ctrl+G. Rail → Expanded: click the chevron, Ctrl+G, or click any group tile (expands with that group selected). Rail + tile: the + tile opens the Create Group dialog without expanding.

## Slide 19
Chapter 3 · B3 icon rail
19
B3 · STEP BY STEP
Slim the column, keep working from the rail
1
Click the chevron
At the bottom of the group column. The column animates from 140 to 40 px (250 ms); the tree fades, the tiles fade in. Layer panel 250 px, canvas +100 px. Tooltip becomes "Expand groups".
2
Read the rail
Top: a + tile in the Create Group style. Below: one tile per group in tree order, labelled G1, G2... or the first two letters of a custom name. Hover shows the full name.
3
Create from the rail
Clicking + opens the same Create Group flow as the full button. The rail stays collapsed; the new tile appears at the bottom.
4
Select from the rail
Clicking a tile expands the column, selects that group in the tree and scrolls it into view. The tile highlight matches the tree selection color.
5
Many groups
More tiles than fit: the rail scrolls vertically with the mouse wheel; a faint fade at the bottom shows there is more.
6
Collapse again
Chevron or Ctrl+G. The rail remembers nothing but the state; selection lives in the tree as before.

## Slide 20
Chapter 3 · B3 icon rail
20
B3 · INTERACTION DETAILS
Making a 40 px rail carry its weight
+
G1
G2
‹
rail: + tile, group tiles, chevron; 40 px wide
1
2
3
1
Create tile
The Create Group button in a compact mode: 30 × 30, "+" label, same black border, same enabled state as the full button.
2
Group tiles
One button per top-level tree item, rebuilt when the tree changes. Label G + index, or two letters of a custom name. Tooltip: full name and member count.
3
Chevron
Bottom of the column in both states, so it never moves under the mouse. Flips › and ‹.
Selection sync
Tile highlight mirrors the tree's current item; clicking a tile calls the same select-and-scroll the tree uses.
Overflow
Rail scrolls; the chevron stays pinned at the bottom outside the scroll area.
Hebrew and persistence
Nothing to mirror except the chevron. GroupPanelRail: true | false in the settings file.

## Slide 21
Chapter 3 · B3 icon rail
21
B3 · ASSESSMENT
B3: still useful when collapsed, smallest gain
For
Collapsed is still functional: Create Group and every group one click away
Control always visible, at the bottom where the mouse already goes
Two states, no hover, works with touch and keyboard
Nothing to mirror for Hebrew except the chevron
Against
Smallest gain: the rail keeps 40 px, canvas gains 100
Tiles need short labels; renamed groups get abbreviated
Many groups means a scrolling rail
Most UI to build: tiles, selection sync, compact Create button
What it takes to build
Rail widget stacked with the tree; width animation 140 ↔ 40
Compact mode for the Create Group button
Tile list rebuilt on tree changes; selection sync both ways
Chevron button pinned at the column bottom
One setting, Ctrl+G, translations
Effort: medium · Risk: low to medium
Canvas +100 px
No hover needed
Effort medium

## Slide 22
Comparison and recommendation
22
SIDE BY SIDE
How the three compare
 | B1 · Pin + peek | B2 · Divider tab | B3 · Icon rail
Control | Faint round pin, bottom far corner, brightens on hover | Chevron tab at mid-height on a draggable divider | Chevron button at the column bottom, always visible
States | Pinned · Auto-hide · Peek | Shown · Hidden (+ any width) | Expanded · Rail
Discoverability | Low at first | High | High
Canvas gain, hidden | +140 px | +134 px | +100 px
Groups reachable while hidden | Yes, hover or click to peek | No, expand first | Yes, tiles stay clickable
Hover dependence | High | None | None
Extra benefit | Panel out of the way but one hover away | Resizable group tree | Create and select without expanding
Hebrew | Mirror pin, strip, slide direction | Mirror chevron | Mirror chevron
Effort / risk | Medium / medium | Small / low | Medium / low-medium

## Slide 23
Comparison and recommendation
23
RECOMMENDATION
Pick B2 now; B1 can sit on top of it later
B2
Build first
Cheapest and safest. Always visible, two states, and it turns the locked splitter into a real one, which also gives a resizable group tree. Nothing about it blocks adding B1 later.
B1
Add if wanted
Once B2 exists, the pin is an extra mode on the same collapsed state: pinned means B2's hidden, auto-hide means B2's hidden plus the peek overlay. The hover delay and click fallback are the parts to get right.
B3
Only if groups are used constantly
Choose this when the goal is a slimmer panel rather than a clear canvas. It does not combine well with the other two, because the rail replaces the hidden state.
Next step: say which one, and the PyQt implementation goes on the same branch: layer_panel.py (inner splitter, widths), main_window.py (shortcut, settings line), group_layers.py (theme colors), translations.py (seven languages).